## Slide 1: HxDS - User Manual > Calculate SNR
Oct., 2019

## Slide 2: UI (1/3)
Detail is only for engineer
After time of setting, it will get data
as signal directly
Threshold to divide signal & noise

## Slide 3: UI (2/3)
Results of Npp/Nave are only useful for Block of Signal type.

## Slide 4: UI (3/3)
Results of Npp/Nave are only useful for Block of Signal type.

## Slide 5: Data Collection – Noise Un-Touched
It caches noise frames to calculate a base data.
Noise and signal data are subtracted base data from Raw Data.
The data is divided into signal and noise by threshold.
The threshold of noise and signal can be modified.
The data frames and ignored frames can be modified.
Threshold
Ignored frames
Noise frames
Signal frames

## Slide 6: Data Collection – Noise Touched
It caches un-touched frames to calculate a base data.
Signal data is subtracted base data from Raw Data.
Signal data and un-touched data are separated from threshold.
Noise data is subtracted the average data of signal data.
The threshold of un-touched data and signal can be modified.
The data frames and ignored frames can be modified.
Threshold
Ignored frames
Base frames
Noise/Signal frames

## Slide 7: Data Collection
Un-Touched
Noise Touched

## Slide 8: Signal-to-noise Ratio – Noise (1/2)
Noise Type | Formula (Delta) | Formula (RAW_DATA)
RMS / SD Average |  | 
Reference | https://en.wikipedia.org/wiki/Root_mean_square | https://en.wikipedia.org/wiki/Standard_deviation
Noise Type | Formula (Delta) | Formula (RAW_DATA)
RMS / SD Average |  | 
Reference | https://en.wikipedia.org/wiki/Root_mean_square | https://en.wikipedia.org/wiki/Standard_deviation

## Slide 9: Signal-to-noise Ratio – Noise (2/2)
Noise Type | Formula
Average of Max | 
Max | 
Npp | 
Nave | 
Noise Type | Formula
Average of Max | 
Max | 
Npp | 
Nave | 
* Data from Raw data may be subtracted base data.

## Slide 10: Example: Raw Data(SD) Noise(1/3)
Step 1: Calculate basedata from untouched n frames
basedata =
10 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 11 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 10
frame n
10
10
10
。。。
10
11
9
。。。
(
) / n = BD0,0
(
) / n = BD1,1
BD0,0 | BD1,0 | BD2,0
BD0,1 | BD1,1 | BD2,1
BD0,2 | BD1,2 | BD2,2
Basedata frame

## Slide 11: Example: Raw Data(SD) Noise(2/3)
Step 2: Calculate SD for each blocks within n frames.
10 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 11 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 10
frame n
10
。。。
(
)/n = SD0,0
) / n = SD1,1
SD0,0 | SD1,0 | SD2,0
SD0,1 | SD1,1 | SD2,1
SD0,2 | SD1,2 | SD2,2
SD frame
2
BD0,0 | BD1,0 | BD2,0
BD0,1 | BD1,1 | BD2,1
BD0,2 | BD1,2 | BD2,2
Basedata frame
BD 0,0
(
)
10
2
BD 0,0
)
10
2
BD 0,0
)
(
10
。。。
(
2
BD 1,1
(
)
11
2
BD 1,1
)
9
2
BD 1,1
)
(
(

## Slide 12: Example: Raw Data(SD) Noise(3/3)
Step 3: Calculate SD Avg.(Noise) by SD frame.
SD0,0
SD0,1
SD2,2
SD0,0 | SD1,0 | SD2,0
SD0,1 | SD1,1 | SD2,1
SD0,2 | SD1,2 | SD2,2
SD frame
。。。
) / 9 = SD AVG(N).
(

## Slide 13: Example: IIR(RMS) Noise(1/2)
10 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 11 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 10
frame n
10
10
10
。。。
10
11
9
。。。
(
) / n = RMS0,0
(
) / n = RMS1,1
RMS0,0 | RMS1,0 | RMS2,0
RMS0,1 | RMS1,1 | RMS2,1
RMS0,2 | RMS1,2 | RMS2,2
RMS frame
2
2
2
2
2
2
Step 1: Calculate RMS within n frames of each blocks.

## Slide 14: Example: IIR(RMS) Noise(2/2)
Step 2: Calculate RMS Avg.(Noise) by RMS frame.
RMS0,0
RMS0,1
RMS2,2
RMS0,0 | RMS1,0 | RMS2,0
RMS0,1 | RMS1,1 | RMS2,1
RMS0,2 | RMS1,2 | RMS2,2
RMS frame
。。。
) / 9 = RMS AVG(N).
(

## Slide 15: Example: Average of Max Noise
12 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 11 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 12
frame n
12
11
12
。。。
(
) / n = Average of Max

## Slide 16: Example: Max Noise
12 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 11 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 10
frame n
12
= Max

## Slide 17: Signal-to-noise Ratio – Signal
Signal Type | Formula
Frame | 
Block | 
* Data from Raw data may be subtracted base data.
Notes: Type Block Fomula說明:
j = 第一張 frame 最大值位置, 後續 frame 取固定位置

## Slide 18: Example: Frame Signal(1/2)
Step 1: Calculate basedata from untouched n frames
basedata =
10 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 11 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 10
frame n
10
10
10
。。。
10
11
9
。。。
(
) / n = BD0,0
(
) / n = BD1,1
BD0,0 | BD1,0 | BD2,0
BD0,1 | BD1,1 | BD2,1
BD0,2 | BD1,2 | BD2,2
Basedata frame

## Slide 19: Example: Frame Signal(2/2)
8 | 0 | 0
-1 | -1 | -1
-2 | -2 | -2
frame 1’
0 | 0 | 0
-1 | 7 | -1
-2 | -2 | -2
frame 2’
。。。
0 | 0 | 0
0 | -1 | 0
-2 | -2 | 6
frame n’
8
7
6
。。。
(
) / n = S
BD0,0 10 | BD1,0 10 | BD2,0 10
BD0,1 11 | BD1,1 11 | BD2,1 11
BD0,2 12 | BD1,2 12 | BD2,2 12
18 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 17 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 18
frame n
Basedata frame
Basedata frame
Basedata frame
Basedata frame

## Slide 20: Example: Block Signal
8 | 0 | 0
-1 | -1 | -1
-2 | -2 | -2
frame 1’
0 | 0 | 0
-1 | 7 | -1
-2 | -2 | -2
frame 2’
。。。
0 | 0 | 0
0 | -1 | 0
-2 | -2 | 6
frame n’
BD0,0 10 | BD1,0 10 | BD2,0 10
BD0,1 11 | BD1,1 11 | BD2,1 11
BD0,2 12 | BD1,2 12 | BD2,2 12
18 | 10 | 10
10 | 10 | 10
10 | 10 | 10
frame 1
10 | 10 | 10
10 | 17 | 10
10 | 10 | 10
frame 2
。。。
10 | 10 | 10
10 | 9 | 10
10 | 10 | 18
frame n
Basedata frame
Basedata frame
Basedata frame
8
0
0
。。。
(
) / n = S
(Subtract basedata frame)
Basedata frame

## Slide 21: Signal-to-noise Ratio – SNR
Type | Formula
dB | 
Ratio | 
Type | Formula
dB | 
Ratio | 

## Slide 22
Drive for better vision

## Slide 23: SNR Calculation Formula